## Slide 1: MCL + Alternative Resources
Ryan Friese, Roberto Gioiosa, Alok Kamatar
PPoPP ‘21

## Slide 2: Tutorial Outline
Some prep work first
  NVDLA background
  Actual hardware + Emulation
Then the fun stuff – performing inference on NVDLA emulators
  pulling the mcl ppopp21 tutorial docker (docker pull minoscomputing/ppopp21)
    If you haven’t done so already go ahead a download now
  Stepping through an example application
  Launching NVDLA emulated devices
  Launching MCL scheduler
  Executing our test app!

## Slide 3: NVDLA – Nvidia Deep Learning Accelerator
Accelerates compute effort of deep learning inference
  4 main groups
    Convolutions
    Activations
    Pooling
    Normalization
  Share a few similar Characteristics
    Regular/Predictable memory access
    Readily parallelizable
Goal: standardized, open architecture for deep learning inference
  Scalable
  Configurable (w.r.t. overall accelerator)

## Slide 4: Nvidia Jetson AGX Xavier
Nvidia developed DLA
Headed implementation
  Controller coprocessor closed source
GPU | 512-core Volta GPU with Tensor Cores
CPU | 8-core ARM v8.2 64-bit CPU, 8MB L2 + 4MB L3
Memory | 32GB 256-Bit LPDDR4x ¦ 137GB/s
Storage | 32GB eMMC 5.1
DL Accelerator | (2x) NVDLA Engines

## Slide 5: Nvidia NVDLA Virtual Platform
The Open Source offering provided by Nvidia (http://nvdla.org/vp.html)
  QBOX: System-C + Qemu based emulation (what we will be using)
  Register accurate emulation
  (although not Virtual, the same open source hardware + software works with FPGAs)
  From our point of view we interact with the emulated devices as if they are network attached accelerators
    We run a lightweight server process on the guest server
  You could conceivably run a full-fledged OS on the guest and interact with as a local accelerator

## Slide 6: DLA Stack
Other DL
frameworks
NVDLA
MCL
Manual memory management, resource selection, kernel launching, etc
TRT Binary Image
POCL
NVDLA Open Source Compiler
Nvdla Binary
NVDLA
Emulator
Manual memory management, resource selection, kernel launching, etc
NVDLA Open Source Runtime
Lightweight Server
Xavier
NVDLA VP
network

## Slide 7: Model Construction and Training
Models implemented using high level ML API’s
Training performed offline
  Potentially on more powerful systems
Networks + Weights serialized
  ONNX
  Caffe
  UFF

## Slide 8: Inference Engine Creation
Ingest network definition & weights
  Or define network manually using TensorRT/OpenSource Runtime
Specify parameters (some dependent on network definition)
  Devices (Which DLA Core, allow GPU fallback)
  Batch size
  FP mode
Serialize inference engine
  NVDLA binary executable
On the Xavier use `trtexec`
On the virtual platform use `nvdla_compiler`

## Slide 9: Model Execution (Inference) on Xavier
Deserialize binary into InferenceEngine
Construct ExecutionContext
Allocate and load input/output buffers
  Unified memory on the Xavier
Create and initialize cudaStream (work queue)
Enqueue inference task
Wait on task completion
Cleanup
All implemented using the TensorRT C++ API
  Also requires some additional bookkeeping and ancillary data structures

## Slide 10: Model Execution (Inference) on Virtual Platform
Create Nvdla Runtime
Load model & Initiate EMU
  This is roughly the equivalent of a ExecutionContext
  Only one model can be loaded at a time (per NVDLA “Core”)
Allocate and load input/output buffers
  A call to allocate a separate call to bind to current model
Submit inference task
  Synchronous operation
cleanup
All implemented using the NVDLA OpenSource C++ API
  There are multiple layers of API available to interact with the devices, we currently are using the highest

## Slide 11: MCL – NVDLA integration
Recall: MCL is built on top of OpenCL
Recall: Tasks are OpenCL kernels (source code) and associated inputs/outputs
  Compiled/executed depending on the device a task runs on
  Devices managed by the MCL Scheduler
NVDLA does not have an OpenCL implementation nor does it compile directly from source
For integration we have developed a custom POCL1 device for the NVDLA
Currently, ingests preconstructed DLA binary
Looking into direct construction from an ML deployment model (e.g. ONNX)
  Would eliminate user needing to run “trtexec” or “nvdla_compiler” or implement a custom serializer
1http://portablecl.org/

## Slide 12: NVDLA POCL Driver
POCL – Portable Compute Language
  Open source implementation of OpenCL standard
Provides the connection between MCL and NVDLA
  Xaiver – calls directly into TensorRT
  Virtual Platform – connects to our lightweight server running in the Qemu image
Device discovery and initialization
Buffer/memory management
Launches and reports finished execution of tasks
Implemented using the OpenCL “builtin_kernel” interface
  Specifies that the device doesn’t run arbitrary OpenCL code

## Slide 13: Time to test it out!
Hopefully by now your docker image has finished downloading
  Recall: “docker pull minoscomputing/ppopp21”
Goal: Take a pretrained mnist (digit recognition) model and use it to performance inference on an (emulated) NVDLA
We will perform the following steps:
  Instantiate NVDLA Qemu devices
  Compile mnist caffe model into an nvdla binary
  Launch MCL scheduler process with POCL envargs to enable NVDLA’s
  Perform inference using an example MCL application

## Slide 14: Instantiating NVDLA Qemu Devices – Host Side
host:~# docker run –name ppopp21 –it minoscomputing/ppopp21 /bin/bash
root@container:/ppopp21# cd nvdla/
root@container:/ppopp21/nvdla#./start_nvdla_emulator.sh 2
We can create multiple emulated NVDLAS!
NVDLA Qemu configuration
Each instance forwards a unique host port
Each instance creates a copy of the virtual hard drive

## Slide 15: Instantiating NVDLA Qemu Devices – Guest side
Mount from the host the directory where this image was launched
Launch the Qemu instance
“expect” is a program that allows us to talk to other interactive application via a script
Insert the NVDLA device driver module into the driver
Launch lightweight server
host:~# docker run –name ppopp21 –it minoscomputing/ppopp21 /bin/bash
root@container:/ppopp21# cd nvdla/
root@container:/ppopp21/nvdla#./start_nvdla_emulator.sh 2

## Slide 16: Instantiating NVDLA Qemu Devices
host:~# docker run –name ppopp21 \
-it minoscomputing/ppopp21 /bin/bash
root@container:/ppopp21# cd nvdla/
root@container:/ppopp21/nvdla# \
./start_nvdla_emulator.sh 2

## Slide 17: Compiling MNIST model to NVDLA format
host:~/#docker exec -it ppopp21 /bin/bash
root@container:/ppopp21/nvdla# make caffe=mnist/mnist.caffemodel \ prototxt=mnist/mnist.prototxt nvdla_emu_bin
# we want our qemu images running so open a new terminal
The process on the Xavier is very similar but uses a different compiler
Nvidia Open Source nvdla compiler
(comes prebuilt on the virtual platform)
Rename from default
Rename from default
In theory NVDLA binaries should be compatible across different implementations assuming the layers with the network are present in the accelerator
We have not (yet) been able to use the same binary on the Xavier and the emulated NVDLA
root@container:/ppopp21# cd nvdla/

## Slide 18: Stripped Down MCL Application (MNIST)
We want to perform inference to predict what digit is present within an image
The only thing we need to (potentially) change is the nvdla binary path to run on hardware vs emulated NVDLAs
The docker container contains a full implementation of this application
Pass DLA binary path
when declaring kernel
Tell MCL this is a kernel binary
Force execution on an NVDLA
Currently compiled offline (previous slide)
root@container:/ppopp21/nvdla# make nvdla_test

## Slide 19: Compiling NVDLA Binary and MCL Executable
host:~/# docker exec -it ppopp21 /bin/bash
# we want our qemu images running so open a new terminal
root@container:/ppopp21/nvdla# make nvdla_test
root@container:/ppopp21# cd nvdla/
root@container:/ppopp21/nvdla# make caffe=mnist/mnist.caffemodel prototxt=mnist/mnist.prototxt nvdla_emu_bin

## Slide 20: Launching the MCL Scheduler
Generally, just need to call
Because we are using POCL + multiple emulated NVDLA we provide a wrapper script to help set some environment variables
mcl_sched
root@container:/ppopp21/nvdla#./launch_mcl_sched.sh
List of devices for POCL to use
POCL device name

## Slide 21: Running our MCL MNIST Inference application
Similar to the MCL scheduler, we must set the same POCL environment variables, so we again wrap the nvdla_test binary in a script
root@container:/ppopp21/nvdla#./run_nvdla_test.sh

## Slide 22: Lets See what Happens!
root@container:/ppopp21/nvdla#./launch_mcl_sched.sh
root@container:/ppopp21/nvdla#./run_nvdla_test.sh

## Slide 23: TL;DR (TL;DW)
root@container:/ppopp21/nvdla#./launch_mcl_sched.sh
root@container:/ppopp21/nvdla#./run_nvdla_test.sh
host:~/# docker exec -it ppopp21 /bin/bash
root@container:/ppopp21/nvdla# make caffe=mnist/mnist.caffemodel prototxt=mnist/mnist.prototxt nvdla_emu_bin
# we want our qemu images running so open a new terminal
root@container:/ppopp21# cd nvdla/
root@container:/ppopp21/nvdla# make nvdla_test
host:~# docker run –name ppopp21 –it minoscomputing/ppopp21 /bin/bash
root@container:/ppopp21# cd nvdla/
root@container:/ppopp21/nvdla#./start_nvdla_emulator.sh 2
Start Emulated NVDLAs
Compile NVDLA & MCL Binaries
Launch MCL Scheduler Execute application

## Slide 24: How about on some real Hardware!?
rfriese@xavier:/ppopp21/nvdla# \
POCL_DEVICES=“nvdla” mcl_sched &
rfriese@xavier:/ppopp21/nvdla# \
POCL_DEVICES=“nvdla” ./nvdla_test
rfriese@xavier:/ppopp21/nvdla# make caffe=mnist/mnist.caffemodel prototxt=mnist/mnist.prototxt nvdla_xavier_bin
rfriese@xavier:/ppopp21/nvdla# make nvdla_test